OXYGEN HANDLING AND STORAGE PROTOCOL

Introduction

This protocol will provide the basic instruction for the safe handling, use and transportation of oxygen within the practice. In all cases, members of staff who will be handling oxygen are to be familiar with the supplier’s instructions for the safe use and storage of oxygen equipment, and are to follow these whenever the equipment is used.

Oxygen supplier: BOC

Routine telephone number:  0800 111 333, available 8am to 6pm Monday to Friday.

Emergency telephone number:  24-hour support service for serious emergencies and incidents, call 0800 111 333

Members of staff not involved with the handling of the equipment are to be familiar with the sections of the supplier’s instructions dealing with safe storage. This protocol is not designed as a substitute for those procedures.

Oxygen may be contained within large cylinders for therapeutic use and / or may be in smaller cylinders contained within emergency bags, response kits etc.

The following basic procedures are emphasised.

Hazard Control

Oxygen supports combustion. Oxygen enrichment of the air can arise unless good handling practices are used. Enrichment of the air by even a small amount can significantly increase the risk of fire caused by heat, sparks, static electricity or other sources of ignition.

Oil and grease can ignite spontaneously in the presence of oxygen, and should not be used to lubricate oxygen equipment, valves etc. The use of handcreams and lubricants of any kind are to be avoided when handling cylinders. No sealant, tape or other means which has not been provided as part of original equipment is to be used.

Smoking is forbidden in areas where oxygen is used or stored.

Storage areas must display an Oxygen storage sign

In the event of a significant escape of oxygen electrical supplies should be isolated at the main supply and potential sources of ignition removed.

In the event of an oxygen fire the use of extinguishers should be restricted to water, dry powder or CO2. Cylinders may be sprayed with water to keep them cool.

Should a cylinder or item require attention or repair, this must only be carried out by the supplier service personnel.

Storage

Store oxygen cylinders:

- securely to prevent the cylinder from falling

- away from areas that would block escape routes or fire exits

- in well-ventilated areas

- away from heat and light sources

- in an area that is not used to store any other flammable materials

- away from combustible material (such as paper, cardboard, curtains)

- so that they are not covered by items of clothing

- Large cylinders should be stored upright

- Small cylinders (e.g. in emergency bags) may be stored indoors, horizontally if necessary, however they should be returned to an upright position as soon as possible prior to use.

Safety advice

- Oxygen can be a dangerous fire hazard. Take adequate precautions while oxygen is being used.

- Do not allow people to smoke where oxygen is being used.

- Keep oxygen at least two metres away from flames or heat sources.

- Do not use flammable liquids, such as paint thinners or aerosols, near oxygen.

- Do not use petroleum based products, such as Vaseline® or Vicks®, near oxygen.

- Make sure that fire alarms and smoke detectors are working.

- Keep a fire extinguisher within easy reach of anyone using oxygen.

Holding stock for emergency use

- If you hold supplies of oxygen for emergency use, you need appropriate equipment and storage.

- Staff must be competent and have appropriate training. They must be able to order, check storage, administer and monitor the effects of oxygen.

- Use a pulse oximeter to monitor the effects of oxygen administration.

- Complete a risk assessment as part of a standard operating procedure or policy.

- Care plans should highlight who can use the oxygen. There must not be a blanket policy for use.

Transportation

Cylinders may be carried within cars subject to the following conditions:

- Only small cylinders for emergency use will be permitted in cars

- While not in use, all valves will be firmly closed and attachments removed

- The cylinders must at all times remain secured and within the transportation bags supplied, in order to prevent damage and movement

- Cylinders will not be used within a car, and must be removed outside if this is to take place

- No smoking is permitted in cars whilst oxygen is being carried

- In the event of a suspected leak the engine is to be stopped and all doors and windows opened to increase ventilation

- Cylinders will not be left in cars where temperatures are likely to be excessive (e.g. in the summer sun)

- A risk assessment hazard data sheet provided by the oxygen supplier is to be kept in the car at all times to be made available to the emergency service in the event of an accident or incident

References

Department for Transport Leaflet: Medical Oxygen in a Vehicle